## Slide 1: Pollynet_Processing_Chain
Zhenping Yin
2019-07-21

## Slide 2: Outline
Workflow
Programs
Products and Configurations
Installation and setup
Future Plan

## Slide 3: rsd server
lacroshome
cloudnet
ceilo
Martha
Bertha
lacroswww
pollyhome
pollydata
Bildermacher
Picasso
Watervapor
pollynet

## Slide 4: PollyNET Workflow
PollyNET processing program
PollyNET Measurements
PollyNET Data Server

## Slide 5: PollyNET Processing Program (PPP)
Automatic calibration
  lidar calibration
  water vapor calibration
  depolarization calibration
Integrated conventional retrieving algorithms
Extensible programming structure

## Slide 6: Rayleigh Fit
Range Corrected Signal:
Attenuated molecular backscatter:
In aerosol-free or nearly aerosol-free (quantitatively?) area, assuming ,
Therefore
Main task is to search the most linear correlated area

## Slide 7: Rayleigh Fit
Normalize the measured signal with attenuated molecular backscatter
Test 1: Pure Rayleigh Conditions
Test 3: White-Noise criterion
Test 4: SNR constrain
Test 2: Near and far range cross criteria
if no other absorptive aerosol layers above it
(Baars et al, AMT, 2016)

## Slide 8: Rayleigh Fit
Normalize the measured signal with attenuated molecular backscatter
Test 1: Pure Rayleigh Conditions
Test 2: Near and far range cross criteria
Test 3: White-Noise criterion
Test 4: SNR constrain
Smaller the mean of the residual is and more Gauss distribution alike the residual is, more possible it could be aerosol-free.

## Slide 9: Shortage of sliding fixed window
Omission: This possible interval will not be found if a large fixed window (like 1 km) was used, since the width of aerosol-free area is only 450m.
More computation: all the sub-areas with a fixed width will be tested.

## Slide 10: Rayleigh Fit – area decomposition
Interested area:
Not intersected
Nearly aerosol-free
Which means the slope of the interested area should be 0 and the shape of interested area should be nearly linear

## Slide 11: Rayleigh Fit - Douglas-Peucker Algorithm
Gifs to show how Douglas- Peucker Algorithm works
Each interval is not intersected.
Each interval is nearly linear, but slope of each interval is still varied.

## Slide 12: Rayleigh Fit
Douglas-Peucker Algorithm
[[z_min1, z_max1], [z_min2, z_max2], … [z_mink, z_maxk]]
Test 1: Slope check
Test 2: Near and far range cross criteria
Test 3: White-Noise criterion
Test 4: SNR constrain
Select the best fit ref interval:
(mean value, standard deviation and slope of the residual, mean square root error from a linear regression, test statistic of Anderson-Darling test)

## Slide 13: Installation and setup: Download
git clone https://github.com/ZPYin/Pollynet_Processing_Chain
This command will download the code from the remote GitHub repository
If you want to develop new features, we recommend you to pull the ‘dev’ branch:
git fetch origin dev:dev
(Detailed information about how to play with `git`, please go to ../doc/git_workflow.pptx).

## Slide 14: Installation and setup: config
PPP global config:
1. setup the global config file from the template
2. edit the global config file
- directories: according to your own requirements.
- ‘fileinfo_new’, ‘doneListFile’, ‘log_folder’, ‘results_folder’ and ‘pic_folder’ will be created automatically
- ‘pollynet_history_of_places_new’, ‘pollynet_config_history_file’ can be found inside the PPP
to control whether to delete the unzipped polly data after each processing.
python 3 folder: PPP uses python3 for data visualization if ‘visualizationMode’was set ‘python’

## Slide 15: Installation and setup: config
PPP add campaign:
Normally, this file was generated from the database. But if there is no connection to the database, you need to add new campaign info manually.
(Be careful about the character of the ‘space’, actually it consists of ‘tab’. So better way is to copy the line before and edit it according to your campaign.)

## Slide 16: Installation and setup: config
PPP add polly config:
Copy the ‘template_config.json’ to a new polly config file with the naming of ‘{polly-type}_config_{date}.json’
You may need to change the settings of:
gdas1Site
AERONETSite
depol_cal_ang_p_time
depol_cal_ang_n_time
meteorDataSource
IWV_instrument
intNProfiles
minIntNProfiles
radiosondeFolder
logbookFile
You can find detailed info about the polly config in /doc/polly_config.md

## Slide 17: Installation and setup: config
PPP create config history: (make sure you setup the info in global file correctly)
PPP edit config history:
config history file works as a lookup table for PPP to search the corresponding polly config file.
better way to do is to copy the line before and then edit it according to your demands.

## Slide 18: Installation and setup: run
Process the measurement results at this moment
Process the measurement results at given day

## Slide 19: Installation and setup
The procedure is valid for (pollyxt_noa, pollyxt_fmi, pollyxt_uw, pollyxt_tjk, pollyxt_lacros, pollyxt_tropos, Arielle, polly_1v2)
Check the ‘pollynet_places_history.txt’ file to ensure the existence of your campaign info
Setup a polly config file under ‘../config’.
Add a new entry for this campaign to link the processing modules with the corresponding config file
Run the ‘pollynet_process_day’
Task from todolist file
Each line represents a task
Pollynet_places_history.txt
Search the campaign info: lat, lon, label
Pollynet_processing_config_history.txt
Search the processing module and config file. (Each polly has its own processing module)
Load the polly config according the ‘Pollynet_processing_config_history.txt’ and activate the processing module